## Slide 1
RV College of
Engineering
Go, change the world
Advanced Digital System Design using Verilog HDL
NAME: RAJAT RAJ USN: 1RV19EC195
Approximate Multiplier Design Using Novel Dual-Stage 4 : 2 Compressors

## Slide 2: Go, change the world
RV College of
Engineering
The power consumption and speed are critical parameters in the design of digital circuits.
Very often, the optimization of one parameter is performed considering a constraint for the other parameter. Specifically, achieving the desired performance (speed) considering the limited power budget of portable systems is challenging task.
Domain: VLSI
Technology: Low Power

## Slide 3: Go, change the world
RV College of
Engineering
This project explores and proposes the design and analysis of two approximate compressors with reduced area, delay and power with comparable accuracy when compared with the existing architectures.

## Slide 4: Go, change the world
RV College of
Engineering
Cameraman
Moon Surface
Result from Exact Multiplication
Result from Approximate Multiplication
X

## Slide 5: Go, change the world
RV College of
Engineering
ARITHMETIC CIRCUIT
MULTIPLIER
PARALLEL
SEQUENTIAL
(low power, their latency is very large)
(such as Wallace tree and Dadda) are fast while having high-power consumptions.
EXISTING METHOD
The multiplier is one of the main blocks, which is widely used in different applications especially signal processing applications

## Slide 6: Go, change the world
RV College of
Engineering
To reduce the delay of the partial product summation stage of parallel multipliers, 4:2 and 5:2 compressors are widely employed.
Compressor chain

## Slide 7: Go, change the world
RV College of
Engineering
The general structure of an exact 4 : 2 compressor is shown in Figure .
It comprises of five inputs, three outputs and two cascaded full adders. A1, A2, A3, A4 and CIN are the inputs and COUT , CARRY and SUM are the outputs of the exact 4:2 compressor.
COUT , CARRY and SUM are given as
COUT = A3(A1 ⊕ A2) + A1(A1 ⊕ A2)
CARRY = CIN (A1 ⊕ A2 ⊕ A3 ⊕ A4) +A4(A1 ⊕ A2 ⊕ A3 ⊕ A4)
SUM = CIN ⊕ A1 ⊕ A2 ⊕ A3 ⊕ A4 (3)
Structure of the conventional exact 4:2
compressor

## Slide 8: Go, change the world
RV College of
Engineering
Multiplication involves mainly 3 steps
Partial product generation
Partial product reduction
Final addition

## Slide 9: Go, change the world
RV College of
Engineering
Power consumption is more .
Area efficiency is less.
Disadvantages

## Slide 10: Go, change the world
RV College of
Engineering
Proposed Method
A novel high speed area-efﬁcient 4 : 2 compressor.
A modiﬁed dual-stage compressor.

## Slide 11: Go, change the world
RV College of
Engineering
The proposed high speed area-efﬁcient 4 : 2 approximate compressor is shown in Figure on next slide.
The compressor inputs are A1, A2, A3 and A4, outputs are CARRY and SUM. A multiplexer (MUX) based design approach is used to generate SUM. Output of XOR gate acts as the select line for the MUX. When select line goes high, (A3A4) is selected and when it goes low, (A3+A4) is selected.

## Slide 12: Go, change the world
RV College of
Engineering
The logical expressions for realization of SUM and CARRY are given below.
SUM = (A1⊕A2)A3A4+(A1⊕A2)(A3+A4)
CARRY = A1+A2

## Slide 13: Go, change the world
RV College of
Engineering
In the high speed area-efﬁcient compressor architecture ,apart from the MUX, one XOR, one AND and two OR gates are required. OR and AND gates each need 6 transistors in CMOS logic implementation.
In order to reduce the transistor count, architecture with NAND and NOR gates are used as shown in Figure.

## Slide 14: Go, change the world
RV College of
Engineering
Approximation is done by eliminating Cout and Cin.
Error has been introduced for the input values − {0011}, {0100}, {1000} and {1111}, so as to ensure that equal positive and negative deviation with ED = 1 (minimum) is obtained.
ED(Error Dist.) refers to the difference between the exact 4 : 2 compressor output and the approximate 4 : 2 compressor output.

## Slide 15
11 Cells, 15 Nets
9 Cells, 12 Nets
8 Cells, 11 Nets

## Slide 16: Go, change the world
RV College of
Engineering

## Slide 17: Go, change the world
RV College of
Engineering
EXISTING METHODOLOGY

## Slide 18: Go, change the world

## Slide 20: Go, change the world
RV College of
Engineering

## Slide 21: Go, change the world
RV College of
Engineering
PROPOSED METHODOLOGY

## Slide 22: Go, change the world
RV College of
Engineering
Proposed 4 : 2 compressors used in 16 × 16 multiplier.

## Slide 23: Go, change the world
RV College of
Engineering
CODE
16bitmultiplerdesign_code_with_testbench

## Slide 26: Go, change the world
RV College of
Engineering

## Slide 27: Go, change the world
RV College of
Engineering
COMPARISON between Existing and Proposed
Existing Model for 16bitmul
Proposed Model for 16bitmul
Area Utilization Report

## Slide 28: Go, change the world
RV College of
Engineering
COMPARISON between Existing and Proposed
Existing Model for 16bitmul
Proposed Model for 16bitmul
Proposed Model for 16bitmul
Power Report

## Slide 29: Go, change the world
RV College of
Engineering
COMPARISON between Existing and Proposed
Max Delay Paths
--------------------------------------------------------------------------------------
Slack: inf
Source: a[1]
(input port)
Destination: p[30]
(output port)
Path Group: (none)
Path Type: Max at Slow Process Corner
Data Path Delay: 17.185ns (logic 6.876ns (40.009%) route 10.310ns (59.991%))
Logic Levels: 18 (IBUF=1 LUT3=2 LUT4=3 LUT5=6 LUT6=5 OBUF=1)
Min Delay Paths
--------------------------------------------------------------------------------------
Slack: inf
Source: a[0]
(input port)
Destination: p[0]
(output port)
Path Group: (none)
Path Type: Min at Fast Process Corner
Data Path Delay: 1.974ns (logic 1.299ns (65.832%) route 0.674ns (34.168%))
Logic Levels: 3 (IBUF=1 LUT2=1 OBUF=1)
Existing Model for 16bitmul
Timing Report

## Slide 30: Go, change the world
RV College of
Engineering
COMPARISON between Existing and Proposed
Max Delay Paths
--------------------------------------------------------------------------------------
Slack: inf
Source: in[4]
(input port)
Destination: z[31]
(output port)
Path Group: (none)
Path Type: Max at Slow Process Corner
Data Path Delay: 15.417ns (logic 5.886ns (38.176%) route 9.532ns (61.824%))
Logic Levels: 18 (IBUF=1 LUT4=3 LUT5=1 LUT6=12 OBUF=1)
Min Delay Paths
--------------------------------------------------------------------------------------
Slack: inf
Source: v[0]
(input port)
Destination: z[0]
(output port)
Path Group: (none)
Path Type: Min at Fast Process Corner
Data Path Delay: 1.974ns (logic 1.299ns (65.832%) route 0.674ns (34.168%))
Logic Levels: 3 (IBUF=1 LUT2=1 OBUF=1)
Proposed Model for 16bitmul
Timing Report

## Slide 31: Go, change the world
RV College of
Engineering
REFERENCES
M. Ha and S. Lee, ‘‘Multipliers with approximate 4–2 compressors and error recovery modules,’’ IEEE Embedded Syst. Lett., vol. 10, no. 1, pp. 6–9, Mar. 2018.
Approximate Multiplier Design Using Novel Dual-Stage 4 : 2 Compressors Pranose J. Edavoor. Sithara Ravenraan, and Amol D. Rahulkar ,IEEE, Mar 2020
H. Jiang, C. Liu, L. Liu, F. Lombardi, and J. Han, ‘‘A review classification and comparative evaluation of approximate arithmetic circuits,’’ ACM J. Emerg. Tech. Comput. Syst., vol. 13, no. 4, p. 60, 2017
I. Alouani, H. Ahangari, O. Ozturk and S. Niar, “A Novel Heterogeneous Approximate Multiplier for Low Power and High Performance”, IEEE Embedded Syst. Lett., vol. 10, no. 2, June 2018, pp. 45-48